## Slide 1
Overview of the MC8 Extension
The Morningstar MC8 can be viewed as a control surface made up of four rows of four footswitches. These are organized into two Pages (in MC8 nomenclature) with each page offering a bottom and top row of footswitches
The GigPerformer MC8 extension allows the user to control widgets linked to VSTs or GigPerformer system functions (e.g., Play/Stop, Tap Tempo, etc.) and select among Rackspaces, Variations, Songs, or Songparts.
The MC8 GigPerformer extension operates entirely within a single Bank on the MC8. One bank on the MC8 must be configured to communicate with the GigPerformer extension. The other 29 MC8 banks will not be utilized or disturbed by this extension.
An MC8 bank programmed with the required Actions is available for download from the GitHub page for this extension.
Controlling GigPerformer with the MC8 Extension
All configuration of how GigPerformer interacts with the MC8 is done by configuring widgets within GigPerformer. This allows Rackspaces to be configured however you would like without having to make any adjustments to the MC8. The goal here is to eliminate any need to keep configurations on the MC8 “in sync” with any changes you make to your Rackspaces, Songs, or Setlists within GigPerformer.
As a result this extension does not use (and cannot use) the “Bank change” actions of the MC8. The extension has its own mechanism and MC8 button press configurations for moving through Racks, Songs, banks, etc. This bears repeating – when interacting with GigPerformer using the MC8 extension you will always be operating through a single MC8 bank and you will never have to modify that bank.
Control Organization
The MC8 is structured with a top and bottom row of switches and corresponding display slots. Each row should be viewed as an independent control group when thinking about laying out your controls. Each row can display and control four widgets, Rackspaces, Variations, Songs, or Songparts at one time.

## Slide 2
Select:
Rotates what is active on row between Widgets, Racks/Songs,
Or Variations/Songparts
Row Down:
Shifts to previous group of what is displayed on this row. e.g., prior four Widgets, Racks/Songs, or Variations/Songparts
Row Up:
Shifts to next group of what is displayed on this row. e.g., next four Widgets, Racks/Songs, or Variations/Songparts
Page:
Moves to Page 2 of the bank, or back to Page 1
A single switch press will toggle or select whatever is assigned to (and displayed near) that switch. This can be anything assigned to a GigPerformer widget, or to select between Rackspaces/Songs or Variations/Songparts (depending on whether GigPerformer is in Setlist Mode)
Any number of Widgets may be designated to be linked to a row of switches. This is done in banks of up to four widgets. Each row of the display can be shifted between functions rotated among banks by using Long Presses of the buttons as indicated below.
The functions are the same but work independently for the bottom and top row, except the Page select.
Long Press actions for controlling the extension

## Slide 3
Select
Row Down
Row Up
Row controls can optionally utilize additional buttons available through MC8 Omniport 1 and 2.
The diagram below illustrates how these are assigned by default.
Row Up
Select
Row Down
Top Row Control
Bottom Row Control

## Slide 4
Widget Configuration
The MC8 extension identifies GigPerformer widgets the user would like to by their OSC/GPScript Name as set in the Advanced tab of the widget editor.
To be controlled by the MC8 extension the GPScript Name must conform to the following format:
mcx_rowID_bankID_[position]
“mcx” identifies it as a widget of interest to the MC8 extension
“row ID” indicates which row of buttons and display this widget will appear on. The choices are:
t = top row
b = bottom row
t2 = top row of page 2
b2 = bottom row page 2
e3 = expression pedal
e4 = expression pedal
“bank ID” is any arbitrary name for this group of widgets that is meaningful to you. Typical examples would be:
fx = general effect toggles
fx2 = a second bank of fx toggles
eq = toggles for different bands on a parametric eq
sys = widgets assigned to GP functions like Play/Stop, Tap Tempo, etc.
“position” must be in the range of 0 – 3 to indicate which switch/display position the widget will appear in. Zero is the leftmost position, 3 is the rightmost
A typical bank of four widgets to appear on the bottom row of page one would be:
mcx_b_fx_0 mcx_b_fx_1 mcx_b_fx_2 mcx_b_fx_3
A second bank of four widgets to appear on the same row would be:
mcx_b_fx2_0 mcx_b_fx2_1 mcx_b_fx2_2 mcx_b_fx2_3
The bankIDs can be rotated through in alphabetical order using the “row up” and “row down” controls.

## Slide 5
Special Configuration Widgets
Several “configuration” widget groups are available to control how widgets appear on the display. These include:
  “Parameter” widgets, which control the names that appear on the MC8 display when values are on or off
  “Indicator” widgets, which can be used to remember which widget banks are active on the MC8 screen when rackspaces, or variations are changed
  “row_configuration” widgets, which tell the extension what functions you want to appear on each of the four MC8 display rows by default (the four rows being “b, t, b2, and t2” as explained previously)
Parameter widgets are optional and correspond 1:1 with the basic mcx widgets previously described. The naming format is identical but with the addition of a “p” character appended to the row_ID.
  Our prior example illustrated basic widgets named as: mcx_b_fx_0 mcx_b_fx_1 mcx_b_fx_2 mcx_b_fx_3
  The corresponding “p” widgets would be named: mcx_bp_fx_0 mcx_bp_fx_1 mcx_bp_fx_2 mcx_bp_fx_3
  If a widget with the appropriate GP Script Name is found it will control what appears on the MC8 display based on the text of the widget Caption as set by the user on the General tab of the widget editor.
  The format of the Caption will be interpreted as “Off name_On name_Long name”
  A typical example would be “Chorus_(Chorus)_Boss CE-2 Chorus”
  This will cause the widget to appear under the name “Chorus” on the MC8 when the widget is off and “(Chorus)” when on. The “Long name” part of the caption is not presently used and may be excluded
  These widget are usually hidden for aesthetic reasons, using the “Hide” option on the General tab in edit mode
  In the absence of a “p” widget the MC8 will display the Caption of the underlying widget when the widget is off, and place a * in front of the same when it is on.
  For example, if the mcx_b_fx_0 widget had a caption of “Chorus” this would appear on the MC8 display as “Chorus” when the widget was toggled off, and “*Chorus” when toggled on
  Note that allowing GP to change the widget caption based on the widget value or temporary values communicated by the underlying VST may produce unreliable results on the MC8 display due to timing issues around reading widget values, particularly during Rackspace and Variation changes

## Slide 6
Indicator widgets are optional and correspond to widget banks. They use an “i” in place of the position indicator.
  Our prior example illustrated basic widgets named: mcx_b_fx_0 mcx_b_fx_1 mcx_b_fx_2 mcx_b_fx_3
  The corresponding “i” widget would be named: mcx_bp_fx_i
  Indicator widgets have two purposes: visually indicating on the Rackspace screen which banks of widgets are currently displayed on the MC8, and controlling which are displayed when a Rackspace or variation is changed.
  The MC8 extension will set this widget to a value of 1 when the indicated bank is actively being displayed on the MC8, and to a value of 0.3 when it is not.
  In our prior example we showed two banks of effects control widgets. These were
    mcx_b_fx_0 mcx_b_fx_1 mcx_b_fx_2 mcx_b_fx_3
    mcx_b_fx2_0 mcx_b_fx2_1 mcx_b_fx2_2 mcx_b_fx2_3
  In the absence of any “i” widgets the MC8 extension will display the group with the bankID that comes first in alphabetical order. In this case the bank “fx” comes before “fx2” and bank “fx” would be displayed when the Rackspace is entered.
  If the Rackspace also contains widgets named “mcx_b_fx_i” and “mcx_b_fx2_i” then the extension can remember which bank you prefer to have selected when you enter a Rackspace or Variation.
  These widgets are often hidden for aesthetic reasons, unless the user has a specific desire to reflect these values on the main Gig Performer screen.
  These are generally created as Text widgets. Because they extension switches the “Value” of these widgets between 0.3 and 1.0 depending on whether they are being shown on the MC8, the apparent brightness of the widgets will change on the GP screen.
  I tend to use Text widgets instead of Shape widgets for this because the Text widget can do everything a Shape widget does, plus some additional features (such as text) than can be hidden (via transparency in the color selector) if not utilized

## Slide 7
Row Configuration widgets are optional and come in two types that correspond to their required names:
  mcx_initial_row_config = control over what functions appear on each row when a Gig file is loaded
  mcx_row_config = same as above but may appear in multiple Rackspaces to configure them differently
  Each of these widgets must have a GP Script Name as indicated above and a caption as follows:
    The Caption is split into four parts with “_” delimiters between them
    Each segment must contain one of: “racks”, “variations”, or “buttons”
    Racks and Variations will be displayed when not in Setlist mode and will automatically switch to Songs and Songparts when GP is put into Setlist mode
    The four positions correspond to what are effectively the four display rows and button banks on the MC8
    The order is b_t_b2_t2 corresponding to bottom and top rows of Page 1 followed by page 2
    My usual configuration is: buttons_variations_racks_buttons which is also the default if no row configuration widget is specified
  If a mcx_row_config widget is present in a Rackspace the MC8 will reflect that configuration upon Rackspace entry
  The user can actively change what is shown on each row at any time using the Select footswitch buttons
  If the Rackspace is then changed to a different Rackspace that does not have a mcx_row_config widget the MC8 will retain the current row configuration
  The the mcx_initial_row_config widget exists for users that want the MC8 switch rows to start with something other than the defaults at Gig loading, but not reset to that default every time a Rackspace is changed. For this reason this widgets should be placed in the Global Rackspace if it is used.
  Note that if an mcx_row_config widget exists in the global Rackspace the extension will pick that up upon every Rackspace change

## Slide 8
Expresion Pedals
Expression in the four Omniports can be assigned to widgets using the same general naming convention as the button widgets.
The format is:
mcx_e1_bankID_0 mcx_e2_bankID_0 mcx_e3_bankID_0 mcx_e4_bankID_0
I use Omniports 1 & 2 for additional control buttons (mine are from American Loopers 3 button models) and I put my expression pedals on ports 3 & 4. This is how the MC8 template bank is constructed.
There is no bank switching mechanism for the expression pedals. If you create more than one bank for any of the four expression pedals there is presently no way to access anything except the first one alphabetically.